## Slide 1: Raspberry Pi GPIO

## Slide 2: GPIO
The Pi has a row of pins along the top edge of the board called General Purpose Input Output(GPIO) pins.
Lets you connect your Pi to other things.

## Slide 3: GPIO Pinouts
The 40 pins on the Raspberry Pi provide various different functions.

## Slide 4: GPIO Pinouts
You'll see pins labelled as 3V3, 5V, GND and GPIO 2, GPIO 3,
Pin Label | Function | Description
3.3V | 3.3 Volts | Anything connected will receive 3.3 volts
5V | % Volts | Anything connected will receive 5 volts
GND | Ground | Zero volts. Used to complete a circuit
GPIO 5 | GPIO pin 5 | These pins are for general input and output and can be used to connect other electonic devices.
ID_SC/ID_SD/DNC | Other functions not addressed here | 

## Slide 5: WARNING:
Randomly plugging wires and power sources into a Pi may destroy it, especially if using the 5V pins.
Bad things can also happen if you try to connect things to your Pi that use a lot of power; LEDs are fine, motors are not.
Make sure to check your circuit is OK before connecting it to the Pi or switching the Pi on.

## Slide 6: Simple Example – Lighting an LED
The LED is connected directly to the 3.3V and GND pins, and should light up. The longer leg of LED should be connected to the 3V3 pin

## Slide 7: Control LED using Scratch
Connect pin 17 to LED (or you can use any numbered pin you wish)

## Slide 8: Control LED using Scratch
Open Scratch on the Pi. Create and run the following program. Before you run it, what will the following program do?